## Slide 1: SCOTSMAN ICE: C1030 – Air & Remote Condenser Units
HIGHLY EFFICIENT, SUPERIOR-PERFORMING ICE SYSTEMS

## Slide 2: Condenser Application Chart
Selecting Ice Machines
Environmental Conditions | Air Cooled (C1030MA-32, C1030SA-32) | Remote (C1030MR-32, C1030SR-32)
Indoor Space Restricted |  | ✓
Poor Ventilation |  | ✓
Indoor Air Temp High |  | ✓
Outdoor Air Temp High | ✓ | 
Water Supply Limited (High sewage cost or sewage limited) | ✓ | ✓
Seeking Low Installation Cost | ✓ | 
Indoor Air Conditioning Capacity Limited |  | ✓
High Water Costs | ✓ | ✓
Noise Level is a Concern |  | ✓

## Slide 3
Air-Cooled
  Recommended clearance of 6 inches on side
  Avoid recirculation
      600lbs. Is tipping point for remote consideration
Remote Ice Machine
  Retro and new construction
      Poorly ventilated areas
      More efficient / consistent production
          Typically 600 lbs. and over
  Roof access
        Licensed contractor for roof penetration
        Line set length and condenser placement
            Maximum rise: 35 feet
            Maximum drop: 15 feet
            Stay within max line set length when possible
Installation Considerations

## Slide 4
Cube Size | Model Number | Condenser Unit | Energy Consumption kWh/100 lb. (45.4 kg)* | 
Medium | C1030MA-32 | Air | 4.83 | $ 10,571
 | C1030MR-32 | Remote | 4.99 | $ 10,471
Small | C1030SA-32 | Air | 4.83 | $ 10,571
 | C1030SR-32 | Remote | 4.99 | $ 10,471
*90°F (32°C) / 70°F (21°C)
C1030 – Air & Remote Condenser Units
Installation & Start-Up Pricing Estimates (1000lb Unit) | 
Air Cooled (C1030MA-32, C1030SA-32) | Remote (C1030MR-32, C1030SR-32)
$675 | $1130*
*If needed, crane fees are in addition to the price listed: (+$500) ----- Exceptions: Union requirements, unique installation requirements such as penetrating walls/roofs, high rise buildings, restricted access, stores in malls or airports and other exceptions are not included and in addition to above costs. Additional costs may be incurred for required permits and/or the removal of existing equipment. | 
70°F
50°F
90°F
70°F
70°F
50°F
90°F
70°F
1077 lbs.
789 lbs.
820 lbs.
996 lbs.
2018 List Pricing