## Slide 1: ICE 101 APPLICATION GUIDE
INTALLATION AND OPERATIONAL CONSIDERATIONS.

## Slide 2
Site Selection
  Power, Water & Drain within 6 Feet
    110, 208-230 Single or Three Phase
  Drain and Water Supply
    Minimum 20 PSI water pressure
    Most local codes require 2 inch air gap for drains
Note: Always Specify Proper Utilities Within 6 Feet
Ice Machine Configuration (Continued on next slide)
Air-Cooled
  Recommended clearance of 6 inches on side
    Less side clearance required for front facing air filter
  Avoid recirculation
    600lbs is tipping point for remote consideration
Installation Requirements
Selecting Ice Machines
Notes: Three Phase is uncommon but uses cheaper wire. There is an up charge for installation.

## Slide 3
Water-Cooled
  Generally prohibited by local code
    Unless on recirculation system
Remote Ice Machine
  Retro and new construction
    Poorly ventilated areas
  More efficient / consistent production
    Typically 600 lbs and over
  Roof access
    Licensed contractor for roof penetration
    Line set length and condenser placement
      Maximum rise: 35 feet
      Maximum drop: 15 feet
      Note: Stay within max line set length when possible
Selecting Ice Machines
Ice Machine Configuration

## Slide 4: Condenser Application Chart
Environmental Conditions | Air Cooled | Water Cooled | Remote
Indoor Space Restricted |  | ✓ | ✓
Poor Ventilation |  | ✓ | ✓
Indoor Air Temp High |  | ✓ | ✓
Outdoor Air Temp High | ✓ | ✓ | 
Water Supply Limited (High sewage cost or sewage limited) | ✓ |  | ✓
Seeking Low Installation Cost | ✓ | ✓ | 
Indoor Air Conditioning Capacity Limited |  | ✓ | ✓
High Water Costs | ✓ |  | ✓
Noise Level is a Concern |  | ✓ | ✓
Selecting Ice Machines