## Slide 1: Technical Service Training
UC2024 and UC2724
Notes: Welcome to a presentation on Scotsman’s self contained ice machines, the UC2024 and the UC2724.

## Slide 2: Service Support
Technical Service 1-800-533-6006
Check out our mobile ready website
www.scotsman-ice.com/service
Notes: Service support is a few clicks away on the internet. Scotsman-ice.com/service.
Scotsman’s recent products are also marked with a symbol that, when read by your smart phone, will take you directly to the service information menu at Scotsman’s website.
At the website there are service manuals, illustrated service parts, and service bulletins.

## Slide 3: Technical Service Virtual Business Card
Notes: Here is an image of a QR code that will connect you directly to the warranty verification section of Scotsman’s website.
While all products are supplied with a user manual, sometimes it isn’t available at the site and, for example, you need to clean the machine. The user manual is on the website and easily found there. So, cleaning instructions as close as your phone.

## Slide 4: Training Agenda
Introduction
Installation
Operation
Maintenance
Diagnostics
Taking the unit apart
Notes: In this meeting you will learn about the UC models. You will learn how to install them. How they work, how to maintain them and a lot of detail on how to take them apart. There will be a diagnostic section to help you find out what the cause of a potential malfunction is. And at the end a look inside.

## Slide 5: UC2024 and UC2724
Cubed Ice Making
  24 inches wide
  39 inches high including legs
  Air or Water Cooled
  Airflow in and out of the front
Notes: Both models are compact, only 24 inches wide and 39 inches high with legs. Cabinets are metal finish and the ice storage bin is injection molded plastic with attached foam insulation.
They are available in either air or water cooled models and breathe in and out of the front panel, so they can be placed next to cabinets on either side. Legs are included.

## Slide 6: Component Location
Air Filter
Notes: All models have an air filter, located at the lower right side of the front panel. Opening the slide – up storage bin door shows the interior, including a compartment cover. That cover, as you will see, covers the ice chute and water reservoir. It also is the mounting for the bin control sensors

## Slide 7: Component Location
Control Box
Fan Motor
Ice Storage Bin
Notes: All have the same layout. The condensing unit is at the bottom, the ice making parts are at the back. Air cooled models have a motor and blade at the left side of the condenser. Water cooled models will have a condenser there with a water regulating valve at the back. Above the condensing unit, the ice storage is in front of the ice making area and the control system is below the bin.

## Slide 8: Component Location
Transformer
Controller Lights and Buttons
Master Switch
Slide Out Electrical Box
Contactor
Notes: Operation is by electronic controller. It is located in the electrical box, which is attached to the underside of the bin support plate.
The electrical box can be slide out for service by removing one retaining screw. After it has been pulled out, the transformer and contactor are accessible in back section.
The controller is attached to the electrical box cover, as is the master switch. There are indicator lights visible thru the overlay on the top of the electrical box cover, and they are only visible when the box has been pulled out.

## Slide 9: Component Location
Drain Hose
Notes: Below the electrical box is the sump drain. It is plugged at the end, and when the plug is pulled out the sump and water pump will be drained.
This plug is used during cleaning, sanitizing or pump removal.

## Slide 10: Component Location
Back Panel Area
Drain
Water Valve
Power Cord
Pump
Compressor
Notes: Ok, what is on the back side? All ice machines need water and drain. The water inlet fitting, a three eighths female pipe, is just below the offset feature of the cabinet. The offset feature provides space for the water and drain tubing, plus if an electrical outlet is located behind the cabinet, space for the power plug.
The drain fitting is a three quarter inch female pipe thread fitting. It is plastic, so if code requires copper, do not sweat the copper while it is installed in the fitting!

## Slide 11: Component Location
Side Views
Flap Switch
Evaporator Thermistor
Notes: With the side panels removed, some important parts are now visible.
One is the flap or curtain switch. It is located on the right side of the unit, under a rubber plug. It is held in with adhesive.
On the other side is the evaporator thermistor. It is attached to the suction line and covered with Armaflex insulation to keep the temperature reading accurate.

## Slide 12: Component Location
Evaporator
Ice Chute
Ice Sensing Flap
Water Distributor
Notes: Looking at the unit from above, you can see at the back, the water distributor, or spray bar, below that is the vertical evaporator.
Below the evaporator is the ice chute, which also contains the ice sensing flap.

## Slide 13: Component Location
Overflow Standpipe
Notes: When the ice chute is removed, the sump is exposed. The red arrow shows the overflow standpipe. It is a fixed height standpipe and drains overflow water during the harvest mode.
Water enters the sump at the left thru the white fitting.

## Slide 14: Component Location
Water Distributor
Back View of Distributor / Spray Bar
Snaps In / Out
Notes: The water distributor or spray bar is a plastic part with many holes. It snaps into a recessed area at the top of the evaporator. Water enters the center back of the recessed area and the bar limits the amount of water flowing over the plate.
The water should flood the plate completely.

## Slide 15: Component Location
Ice Chute
Ice Chute
Notes: The ice chute is positioned at the bottom of the vertical evaporator, and is angled down towards the storage bin. In it is the ice sensing flap, normally open.

## Slide 16: Component Location
Ice Sensing Flap
Flap Open (Freeze)
Flap Closed
(Harvest or Bin Full)
Magnet
Notes: The ice sensing flap has a magnet on the right end. The flap is normally open, allowing water to return to the sump after flowing over the evaporator.
When ice is released, the ice slides down the ice chute as a unit and goes over the flap, closing it. That moves the magnet back and up. The flap or curtain switch is positioned across from where the magnet is when the flap is closed.

## Slide 17: Component Location
Ice Sensing Flap and Switch
Notes: As the flap moves down to a closed position, the magnet moves up and back towards the flap switch.
When the flap magnet and flap switch are aligned, the switch closes, triggering the end of harvest.
If the flap stays closed for a few seconds, the unit shuts off on bin full.

## Slide 18: Installation - Utilities
Recessed area
  Power cord
    5-15P plug
  Water fitting
    3/8” FPT inlet on 60Hz
    Remember to flush the line!
  Drain fitting
    3/4” FPT
    Vent horizontal runs
Notes: All models require power, water and drain. Their connections are in a recessed area of the back. The power cord for 115 volt models is ready to be plugged into a standard 15 amp outlet. The water fitting on the back is a 3/8 female pipe thread. It is a good idea for any installation to flush the water supply line, because in old plumbing there is scale on the inside of the tubing that can become loose after being disturbed and new tubing can have debris in the tubes. The drain fitting is ¾ inch female pipe thread. When water cooled another water inlet and drain connection are also located in the same area. If the tubing outside the machine has a long horizontal section, additional venting may be needed for proper draining.
This NSF satisfied model does not need a back flow preventer, but one could still be required by local health inspectors.

## Slide 19: Water Filtration and Treatment
Taste and Odor Filters
  Use if water has objectionable taste
  This type contains activated carbon
  T&O Filters remove chlorine
    Chlorine frequently added by water treatment plant to kill bacteria
Risk of increased bacteria growth by using a Taste and Odor filter
  Other types available
Notes: Potable water is required to be supplied to the machine but DI water is not recommended. While it is a good idea to install a water filter, a taste and odor filter usually contains activated carbon to remove tastes, including chlorine. The chlorine has probably been put there to purify the water and when removed that barrier against bacteria is also removed, so increased bacteria growth can occur with that type of water filter. There are other types available that usually only filter and treat the water for minerals.

## Slide 20: Installation
Place in planned location
  Must have water, drain and power nearby
Level the unit
  Use the included legs
    Leg thread is 5/8 – 11
  Or seal the cabinet to the floor
    Rubber bumpers on the bottom reduces floor damage
Notes: Legs may be used, there are threaded nuts in the base for leg attachment. Most health codes require legs or, if legs are not used, the cabinet must be sealed to the floor.
Once the unit is in the installed location, level it using the adjustments provided in the legs.

## Slide 21: Pre-Start Check
Remove front panel
Remove shipping block under fan motor bracket
Check for any other shipping materials
Notes: Take the front panel and compartment cover off to confirm that all the hoses are connected, no tubes are rubbing each other and that there are no loose parts or screws.

## Slide 22: Installation – Start up
Turn on water supply
  Confirm no leaks
Connect power, move master switch to ON
  Anti-Slush light blinks for 90 seconds
  After that, the unit will move to Harvest mode for 90 seconds
    Water flows in
    Compressor turns on
    Hot gas valve opens
Freeze begins- pump and fan turns ON
  Water and hot gas valves turn OFF
Notes: Start up or restart takes some time, as the unit needs to be ready to be in ice making mode. It needs to have the compressor ready to start, and it needs to have the sump full off water.
At first it appears that nothing is happening, but if you have the electrical box slid out you will see that the Anti-Slush light is blinking. It does that for ninety seconds. Then the inlet water solenoid valve, the hot gas valve and the compressor are energized. This continues for another ninety seconds.
Then the freeze cycle begins, the water pump starts. The inlet water solenoid and hot gas valves close. And, after head pressure has built up, the fan will begin to turn.

## Slide 23: Installation – Start up
Check bin control for shut off
  Move flap to closed and then open
  See the Bin Full light blink
Pour water in bin, check draining
Return front panel to unit
Notes: You should check that moving the ice sensing flap makes the Bin Full light blink.
Also pour water into the bin to be sure there are no leaks.

## Slide 24: Controller
Four Status Lights
  Timer
  Freeze
  Bin Full
  Anti-Slush
Ice Bridge Thickness Degree Lights
  More lights = Thicker Ice
Notes: Timer On
• This light is switched ON when the freeze cycle has progressed significantly enough for the evaporator thermistor to have reached its freeze preset temperature. At this point there are only a few minutes left in the freeze cycle. It is also switched ON when the harvest cycle has been on and the evaporator has reached its set defrost temperature.
Bin Full
• Normally OFF. This light is switched on and off by the position of the ice sensing plate.
Freeze Mode
• Normally ON during a freeze cycle. OFF during harvest or ice release.
Anti Slush Mode
• Normally OFF. This light is switched ON when the pump is stopped during a freeze cycle.

## Slide 25: Ice Thickness Degree Lights
10 settings on 5 lights
1 blinking is minimum, 5 steady is maximum
  – Steady light = 2
  – Blinking light = 1
Examples
  3 lights on steady = 6
  3 lights steady, 1 blinking = 7
Adjust before timer light is on or wait till next cycle
Notes: Each push and release of the + or - button will change the lights that glow or blink indicating a change in ice size.
Example: pushing + one time changes a blinking light to steady on type. If the lights are on steady a single push of + will add one more light and it will blink.
There are 10 settings. All 5 lights on steady is the maximum setting and one blinking light is the minimum.

## Slide 26: Normal Bin Full
Notes: This image shows, from above, how the ice fills the bin and what it appears like when full.
The image shows the sensing flap in the closed position, held closed by the ice on top of it.
When the user uses the ice, the ice on the chute will slide off and the unit will restart.

## Slide 27: UC2024 Operation
Data is for new, clean machines
R-134a (PSIG) |  |  |  |  | 
Conditions | Suction, just before harvest (minutes) | Max Discharge in harvest (seconds) | Cycle Time (minutes) | Freeze Cycle (minutes) | Harvest Cycle (seconds)
70/50 | 6 - 7 | 48 | 15 - 16 | 14 - 15 | 50
90/70 | 6 - 7 | 60 | 19 - 20 | 18 - 19 | 35
Model | Compressor Amps
UC2024 | 6 – 6.5
Notes: They operate with refrigerant R-134a. Some important refrigeration pressures are in the table, they are the maximum discharge pressure in harvest and the suction pressure just before harvest.

## Slide 28: UC2724 Operation
Data is for new, clean machines
Model | Compressor Amps
UC2024 | 6 – 6.5
R-134a (PSIG) |  |  |  |  | 
Conditions | Suction, just before harvest (minutes) | Max Discharge in harvest (seconds) | Cycle Time (minutes) | Freeze Cycle (minutes) | Harvest Cycle (seconds)
70/50 | 3 - 4 | 52 - 54 | 13 - 14 | 12 - 13 | 50
90/70 | 4 - 5 | 65 - 68 | 17 - 18 | 16 - 17 | 40
Notes: They operate with refrigerant R-134a.

## Slide 29: Example Cycle
Chart: System Pressures 70/50
Notes: This graph shows the pressures during a typical 70/50 cycle. You can see that both discharge and suction pressures decline during the cycle, and you can see the slight change during Anti-Slush when the pump is off.

## Slide 30: Example Superheat
Notes: What is the superheat? That is a common question, but the answer is “it depends.” Where in the cycle is a main item, as the superheat declines as the freeze cycle progresses.
This graph shows superheat in a freeze cycle. Note that it varies a lot at the beginning of the freeze cycle. It is affected by the prior harvest cycle, where it was negative, the anti-slush period and when the fan cycles.
Five minutes into freeze is at a fairly stable point, and it is about 13 degrees then, for this unit, a UC2024 at 70/50.

## Slide 31: Maintenance
Flush out drain
Clean Filter - Pull air filter out
  Wash off, dry and return
  Also in water cooled
    For appearance only
Notes: All ice products require maintenance. Other maintenance is routine cleaning of the air filter to remove lint, water and ice making system lime scale removal and sanitizing and dispense system cleaning and sanitizing. The air filter is located on the right side of the cabinet, it is easily removed by pulling it to the right. It is a washable filter. It is also found in the water cooled models, but there it is only for appearance.

## Slide 32: Water System Maintenance
Scale Removal
Sanitizing
Notes: Water system maintenance includes removing the scale that builds up during ice making. Scale is from the minerals in the water supply and many times is limestone. Limestone is a rock and that hard material must be dissolved by acid, which is what ice machine scale remover is.
Because ice is a food, it is critical to also sanitize the system frequently. 6 months is an industry standard for cleaning, local conditions may require more frequent cleaning. The machine will not be kept clean without someone providing the necessary maintenance.

## Slide 33: Scale Removal
Remove front panel
Move master switch to OFF
Discard ice
Drain sump
Notes: Begin with scale removal. Remove the front panel and switch the unit off. Do not disconnect from power.
Discard all ice that may be in the bin.
Drain the sump by pulling the drain plug on the end of the hose.

## Slide 34: Scale Removal
Drain water system
  Pull sump drain hose plug
  Reconnect hose plug when done
Notes: The next step is to drain the sump. There is a drain hose attached to the sump and evaporator, its end is located below the controller. Pulling the plug releases the water, direct it into the bucket then reconnect the plug.

## Slide 35: Scale Removal
Mix a solution of 5 oz or 150 cc of Scotsman Clear 1 Scale Remover and 2.5 quarts or 2.4 liters of clean, warm potable water.
Do NOT mix any stronger!
Notes: Mix a solution of 5 ounces of Scotsman Clear 1 scale remover and two and a half quarts of clean, warm potable water.
Do not mix the solution any stronger! More is not better!

## Slide 36: Scale Removal
Remove water distributor and ice chute from unit.
Wash them with the scale remover solution and return them to the unit.
Notes: Remove the water distributor and ice chute from the unit, wash them in the scale remover solution and return them to the unit.
These parts are cleaned first because they are the most likely to have scale build up and they could affect how the cleaning solution is distributed in the wash step.

## Slide 37: Scale Removal
Pour the scale remover mixture into the sump
Notes: Pour the scale remover solution into the sump.

## Slide 38: Scale Removal
Move the master switch to Wash
Operate the unit in the Wash mode for 20 minutes or more
Move the master switch to OFF
Notes: Run the unit in the wash mode for at least 20 minutes to circulate the scale remover solution thru the pump, pump hose, water distributor, evaporator, and ice chute.
If the machine does not appear clean enough at 20 minutes, run it longer.

## Slide 39: Scale Removal
Drain water system
  Pull sump drain hose plug
  Reconnect hose plug when done
Notes: The next step is to drain the sump. Pulling the plug releases the water, direct it into the bucket then reconnect the plug.

## Slide 40: Scale Removal
Check water distributor for any remaining scale, repeat cleaning if needed.
Wash the bin with scale remover solution.
Flush the bin drain with hot water.
Notes: The water distributor has many small holes, be sure they are all clear and open. If needed, repeat the wash step with more cleaning solution.
Wash the bin with scale remover solution.
Flush the bin and bin drain with hot water.

## Slide 41: Sanitization
Use locally approved sanitizer.
  Mix 2 to 2.5 gallons of solution per directions of the sanitizer
  Pour sanitizer solution into sump until full
  Move master switch to Wash
  Operate the unit in Wash for 10 minutes
  Move the master switch to OFF
Notes: So far we have acid cleaned the ice maker. Now we will sanitize it. This process is slightly different. Begin by mixing 2 gallons of sanitizer. Some sites have requirements for the brand and type of sanitizer, use what is locally approved. Pour the sanitizer solution into the sump until it is full.

## Slide 42: Sanitization
Drain water system
  Pull sump drain hose plug
  Reconnect hose plug when done
Notes: The next step is to drain the sump. Pulling the plug releases the water, direct it into the bucket then reconnect the plug.

## Slide 43: Sanitization
Move master switch to ON to restart ice making
Make a batch of ice
Pour hot water into bin to melt ice until ice is gone
Reattach all panels
Notes: This is the last part of cleaning. We want to make some fresh ice and melt it, so reconnect power and restart ice making.

## Slide 44: Sources of Ice Machine Service
Notes: Most ice machine service is from the main ingredient of ice: Water.
Water is used with an electrical control system and mechanical refrigeration to make ice. Without water, there is no ice. But with water comes impurities like calcium carbonate and other minerals. During ice making, especially in a cuber, the pure water freezes first, leaving the impurities in the unit. That is why there is a flush system of some type in nearly all commercial cubers and many residential ones too.
Of course, the electrical components can fail, as can refrigeration. But mostly you will be dealing with lime scale, water filters and the maintenance needed.

## Slide 45: Diagnostics
No Ice
  No water in sump
Check for
  Plugged water filter
  Inlet water solenoid valve not opening
Notes: You have a no ice service call. When you arrive you find there is no water in the sump. Why is that? It can be from a plugged up water filter, maybe it hasn’t been changed in a few years. Or the inlet water solenoid valve did not open. What other causes can you think of?

## Slide 46: Diagnostics
No Ice
  All components operating
Check for
  Inlet water valve leaks through
  Hot gas valve leaks through
    Water is warm
Notes: Its another no ice call, this time everything is working, there is water in the sump and the pump is moving the water over the evaporator plate.
So, what could be wrong? One possibility is there is excessive heat load, probably from an inlet water solenoid leaking water into the machine all the time.
Or, more rarely, the hot gas valve does not shut off tightly, so it leaks hot discharge gas into the evaporator. Since there is water being pumped over the evaporator, the sump water will be warm, not cold.

## Slide 47: Diagnostics
No Ice
  In freeze, anti-slush light is OFF
  Water in sump
  No water over evaporator
Water is part of the recipe!
  Check pump
    Move master switch to Wash
    Check for water over plate, if none, check voltage at pump
    If water over plate, replace controller
Notes: No ice again. The unit is in a freeze mode, the anti slush light is OFF. Water in the sump, but no water being forced to the top of the evaporator.
You need water for ice. This sounds like a water pump not working. Check for voltage to the pump, if there is voltage at the line terminal, the pump motor is not working and the pump should be replaced.
If no voltage, switch the master switch to Wash and recheck, the water begins to be pumped, the controller is not connecting power to the pump circuit and should be replaced.

## Slide 48: Diagnostics
No Ice
  Bin full light is ON: False bin full
Check for
  Flap in closed position
  Flap switch stuck closed
    Note: Labeled curtain switch in wiring diagram
Notes: No ice in the bin, the unit is off, but the bin full light is on. This is a false bin full condition.
Check the ice sensing flap for being stuck in the closed position. It can also be a failed flap switch, which is called a curtain switch in the wiring diagram.

## Slide 49: Diagnostics
Makes ice, but much too large or too small
Check for
  Cube size set to incorrect size
  Thermistor failure
    Operating on timed cycles
    Indicated by all cube size and harvest time lights are flashing
Notes: This unit makes ice but it is either too large or to small.
A first thought is that the cube size is set wrong. But when you try to adjust it you find that all the cube size and harvest time lights are flashing on and off. This is a signal of thermistor failure. Replace the thermistor set.

## Slide 50: Diagnostics
No ice in bin
  Makes ice, but does not release from plate
Check for
  Ice bridge too large
  Hot gas valve not opening
  Evaporator plate damaged
Notes: This unit makes ice but does not release them into the bin, so there is no ice. It can be that the ice is much too large to be released, it is frozen to the sides of the plate. Or it can be that the hot gas valve does not open, so there is no heat available to melt the back side of the cube.
A more remote possibility is that the evaporator is damaged, it could be the plating or it could be the tube separating from the plate.

## Slide 51: Diagnostics
No ice
  Air cooled fan not turning
Check for
  Open windings on fan motor
  Seized fan motor
  Fan pressure control not closing
    opens at 100 PSIG, auto reset closed at 150
Notes: This is most likely to occur only when the cooling media has quit flowing – no water or no air. So check for water or recirculating coolant being shut off or a failure of the air cooled fan motor.

## Slide 52: Diagnostics
No ice
  Unit in ice making mode (freeze light is ON) but contactor is not pulled in
Check for
  Open contactor coil
  No power to contactor from controller
  High pressure cut out open
    Opens at 400, auto reset closed at 300
Notes: It is no ice again, this time there is no refrigeration. You find that the contactor is not pulled in.
This can be from a few causes.
Begin by checking for power to the coil, if there is the contactor coil is probable open. If no power, it may be that the high pressure cut out is open. It opens when the discharge pressure reaches 400 psig, and automatically recloses at 300 PSIG.
A remote possibility exists that the controller has not connected power to the contactor circuit and should be replaced.

## Slide 53: Diagnostics
No ice
  Compressor off, pump forcing water over evaporator
Check for
  Overheating
    Low charge
    High superheat
  Contactor coil open
  Compressor not starting
    Start relay or PTCR
    Start capacitor
    Motor windings
Notes: Proper diagnostics are the key to a short and successful service call. Finding the root cause of the malfunction and correcting just it are critical.
A no ice call is likely to be the most common type on an ice machine.
When a compressor is off and the unit not in a start up mode, check the contactor, as in the slide before, and if it is closed, the compressor needs a diagnostic check.
This compressor is similar to other compressors you’ve seen. It has a motor, starting components and valves. Most techs will have no issues in obtaining a proper diagnosis, yet the compressor suppliers say, of the warranty compressors they analyze, that some are not defective and should not have been replaced.
Scotsman has an excellent compressor troubleshooting flow chart on its website, if you are used to flow charts, it can be a help.
An overheating compressor will shut down on its internal overload. It can take a long time before it cools down enough to reclose, so when its open, the compressor appears to have open windings.
The compressor could overheat from a lack of refrigerant. It is a refrigerant cooled motor, and if the TXV starves it, or the charge is low, the compressor will overheat.
Starting components are needed to start the compressor. The PTCR or start relay must connect power to the start winding. The start capacitor must be checked if the compressor will not start.

## Slide 54: Test Mode
To use test mode (pump will be off in Test Mode):
  Place both thermistor probes in 32oF. water.
  Push and hold the left plus (+) button and the lower right minus (-) button for at least 5 seconds. Then release them. The yellow LED will light up for 3 seconds.
  Push and release the left plus (+) button. The yellow light will switch on if the evaporator thermistor resistance is correct.
  Push it again and if the water thermistor resistance is correct, the yellow light will switch on.
  Push and release the right plus (+) button. The blue light will switch on.
  Push it again and the red light will switch on.
  Push and hold the right minus (-) button. The green lights will switch on one at a time as long as the button is pushed in. Release when completed.
  Push and release the right minus (-) button. The yellow light will switch on, indicating correct system memory.
Disconnect electrical power to end test mode
Notes: The controller has a test mode, it is useful for testing the thermistors.

## Slide 55: Taking the Unit Apart
Remove front panel
Drain water system
Notes: Taking the front panel off exposes the ice storage bin, controller and condenser.
Be sure to drain the water system.

## Slide 56: Taking the Unit Apart
Remove top panel
  Three thumb screws at back
  Push panel back slightly
  Lift up and off
Notes: Removing the top panel begins by taking the three thumb screws off at the back. They should have been removed when the back panels were taken off.
Then push the top panel back slightly so it releases from the screwheads in its keyhole slots, then lift up and off the cabinet.

## Slide 57: Taking the Unit Apart
Bin is not removable
Removing left, right and back panels helps with access
Water inlet solenoid valve is at the back
Hot gas valve is at the back
TXV is at the back
Notes: Service access is improved with the panels off. But note that the bin is not removable and many components are at the back, so the unit will need to be pulled out for service.

## Slide 58: Taking the Unit Apart
Flap/Curtain switch is under the right side panel
Notes: The flap or curtain switch is in a recessed area on the right side of the cabinet. It is under a rubber plug, and is held down to the foam insulation by adhesive.

## Slide 59: Taking the Unit Apart
Water thermistor is at the back
Water pump is at the back
Evaporator thermistor is under the left panel
Notes: The water thermistor is in the pump discharge hose at the back of the cabinet. The evaporator thermistor is shown here with its insulation removed. It is clipped to the suction line at the corner of the cabinet.
Thermistors are replaced as a set.

## Slide 60: Taking the Unit Apart
Water pump
Notes: The water pump is located at the back. It is held by a rubber mount. The hoses pull off the inlet and outlet.
Be SURE to drain the sump before taking the hoses off.

## Slide 61: Taking the Unit Apart
Evaporator
Notes: The two arrows are pointing to two screws that hold the evaporator assembly in the unit.
Once the refrigerant has be recovered from the machine, the refrigeration tubing separated, and these two screws removed, the evaporator slides up and out of the unit.

## Slide 62: Taking the Unit Apart
Compressor
  Behind lower back panel
Notes: Replacing the compressor is done from the back.
1. Disconnect Electrical Power
2. Remove front and lower back panels.
3. Remove top and right side panels.
4. Recover refrigerant
5. Remove electrical connections from compressor
6. Unsweat process, suction and discharge tubes from compressor.
7. Remove fasteners holding compressor to base and lift compressor from unit.
8. Confirm new compressor is the correct one for the unit.
9. Remove old dryer from unit.
10. Place in unit.
11. Braze the suction, discharge and process tubes onto the new compressor using the methods and procedures of the refrigeration trade for that work.
12. Braze a new dryer into the liquid line where the original one was.
13. Evacuate the system to 300 microns.
14. Weigh in the nameplate charge.
15. Attach the electrical connections to the compressor.
16. Restart and test for proper operation.

## Slide 63: Taking the Unit Apart
Fan
  Removable from the front and with the left panel off
  Access holes for easy access to back screws
Notes: The condenser fan motor only operates when the fan pressure control closes to connect power to it. Before changing a fan that does not turn, check for power to it first.
To replace:
1. Disconnect electrical power to the unit.
2. Remove the front and left side panels.
3. Disconnect the quick connect to the fan motor.
4. Use a long screwdriver and the slots on the side to remove the hard to reach screws holding the plastic venturi to the condenser shroud.
5. Pull the fan motor and venturi out and remove the fan motor and assembly from the unit.
Note: The fan motor is only available with the blade and venturi.

## Slide 64: Technical Service: 1-800-533-6006
www.Scotsman-ice.com
Notes: Service support is a few clicks away on internet. Scotsman-ice.com, select service support. There are 6 main points of access, including parts lists and bulletins.

## Slide 65: Questions?