## Slide 1: INTRODUCING UNDERCOUNTER FLAKE & NUGGET
SMALL IN STATURE, BIG ON PRODUCTION.

## Slide 2
Undercounter Flake & Nugget Models
Nugget & Flake Ice: 15” & 20” wide units now available
Get the nugget and flake ice your customers love anywhere you need it with Scotsman’s new Nugget and Flake Undercounter Units. With a proven freezer design and sealed bearings—you’ll have everything your facility requires in a more compact design.
NEW!

## Slide 3
New Product Release Information
Flake & Nugget Units (15”, 20”)
Estimated shipping release is week of December 16th
Pre-orders for new units are now being accepted

## Slide 4
New Product Launch Kit
Initial Content Package
Now available for download:
Resource Center -> Product Information
Contains:
Product photography
  Includes environmental and 360° imagery
Literature
  Specification sheets
  Sell sheet
  Brochure
A+ Enhanced Content
  Visual based marketing graphics that are ideal for ecommerce
Videos
Cross Reference Document
  Helps to link which files correspond to each model
  Also includes easy to import specification information
More content/marketing materials will be released closer to launch date

## Slide 5
New Product Competitive Comparison
15” Flake & Nugget Units
64% larger storage capacity
36-62% more energy efficient
New to Industry:
There are currently no competitive comparisons
for a 15” undercounter flake machine

## Slide 6
New Product Competitive Comparison
20” Flake & Nugget Units
90% larger storage capacity
21% more energy efficient
14% larger storage capacity
13% more energy efficient

## Slide 7: Undercounter Flake & Nugget: Overview

## Slide 8: Undercounter Flake & Nugget: 15” Platform
UF0915
Air Cooled
115 V / 60 Hz
Energy Star® Certified
Optional KUFM15 floor mount kit
Capacity: 76 @ 90°/70°
96 @ 70°/50°
Storage: 36 lb.
Dimensions: 15” x 24” x 38”
Includes legs, scoop,
and 5.5’ power cord
UF1415
Air Cooled
115 V / 60 Hz
Energy Star® Certified
Optional KUFM15 floor mount kit
Capacity: 107 @ 90°/70°
142 @ 70°/50°
Storage: 36 lb.
Dimensions: 15” x 24” x 38”
Includes legs, scoop,
and 5.5’ power cord
UN0815
Air Cooled
115 V / 60 Hz
Energy Star® Certified
Optional KUFM15 floor mount kit
Capacity: 55 @ 90°/70°
79 @ 70°/50°
Storage: 36 lb.
Dimensions: 15” x 24” x 38”
Includes legs, scoop,
and 5.5’ power cord
UN1215
Air Cooled
115 V / 60 Hz
Energy Star® Certified
Optional KUFM15 floor mount kit
Capacity: 84 @ 90°/70°
119 @ 70°/50°
Storage: 36 lb.
Dimensions: 15” x 24” x 38”
Includes legs, scoop,
and 5.5’ power cord

## Slide 9: Undercounter Flake & Nugget: 20” Platform
UF2020
Air Cooled
115 V / 60 Hz
Energy Star® Certified
Optional KUFM20 floor mount kit
Capacity: 149 @ 90°/70°
216 @ 70°/50°
Storage: 57 lb.
Dimensions: 20” x 24” x 38”
Includes legs, scoop, and 5.5’ power cord
UN1520
Air Cooled
115 V / 60 Hz
Energy Star® Certified
Optional KUFM20 floor mount kit
Capacity: 125 @ 90°/70°
167 @ 70°/50°
Storage: 57 lb.
Dimensions: 20” x 24” x 38”
Includes legs, scoop and 5.5’ power cord

## Slide 10: Undercounter Flake & Nugget: 24” Platform
UF424 (Replaced AFE424)
Air and water cooled
50 and 60 Hz options
Optional KUFM24 floor mount kit
Capacity: 310 @ 90°/70°
440 @ 70°/50°
Storage: 80 lb.
Dimensions: 24” x 28.5” x 39”
Includes legs, scoop, and 5.5’ power cord
UN324
Air and water cooled
50 and 60 Hz options
Optional KUFM24 floor mount kit
Capacity: 266 @ 90°/70°
340 @ 70°/50°
Storage: 80 lb.
Dimensions: 24” x 28.5” x 39”
Includes legs, scoop and 5.5’ power cord

## Slide 11: Space Saving Design: ADA Compliant
31.9”
38”
20”
With legs
Without legs
With use of KUFM20 floor mount kit
20”
31.9”
38”
Without legs
With use of KUFM15 floor mount kit
With legs
15”
15”
15” Platform
20” Platform

## Slide 12: Space Saving Design: Recessed Utility Chase
With legs
33.5”
24”
39”
24”
Without legs
With use of KUFM24 floor mount kit
24” Platform
Recessed utility chase on backside of unit provides clearance along the wall for tight installs

## Slide 13: Space Saving Design: Front Breathing
No Side Clearance Required
Maximizing ice output despite a small footprint
Front air intake and exhaust
No side clearance required allowing for flexible placement in the tightest locations
Machine can be placed directly beside walls and other equipment

## Slide 14: Ease of Use: Simple Servicing
AutoAlert™ Indicator Lights
Cleaning and service information can be conveniently found upon removing the front panel
Innovative LED indicator lights keep operators informed of unit’s status
Signals staff when it is time to descale, sanitize and more
Each of the 4 lights labeled with an easy-to-identify icon

## Slide 15: Ease of Use: QR Code
Quick Response (QR) Code
Every Essential machine features a QR code that connects customers to vital unit specific information
Helps reduce downtime and frequency of service calls
QR code leads to a warranty registration page, auto-populated with the corresponding serial number

## Slide 16: Ease of Use: QR Code
Quick Response (QR) code
Operators and service technicians can use their smart phone to scan the QR code to access instant warranty and technical information specific to that model
The product serial number will automatically populate the page
SCAN WITH YOUR SMART PHONE
Scanning Tip:
Some recent phone updates allow you to use your phone’s built-in camera app to scan QR Code

## Slide 17: Ease of Use: Ergonomic Bin Door
Convenient Slide-Up Door
Machines feature a durable, slide-up door that provides convenient and easy access to the ice bin

## Slide 18: Ease of Use: Quick Installation
Included in the Box
5.5’ power cord with NEMA 5-15P plug
Ice scoop
6” adjustable legs

## Slide 19: Flake & Nugget: Superior Reliability
Maintenance-Free Bearing
The Problem: Components used to create compressed ice require maintenance for routine checks, specifically with wearable parts like bearings
Innovation: All UF/UN models feature a proprietary, maintenance-free bearing, fully sealed with a high-tech polymer that lubricates and eliminates the need for greasing (launched in 2015)
Exclusive technology uses no wearable parts and no grease, which decreases potential service and maintenance issues

## Slide 20: Flake & Nugget: Superior Reliability
Heavy-Duty Stainless-Steel Components
Scotsman Nugget and Flake undercounter units feature:
  An extremely reliable stainless-steel evaporator
  Durable stainless-steel auger
Ensures maximum durability and reliability for a long machine life

## Slide 21: Flake & Nugget: Superior Reliability
Designed for Maximum Lifespan
Aluminum alloy side and top panels
  Corrosion resistant
  Easy to clean, smudge resistant
Hard plastic front panel
  Durable and rust-free

## Slide 22: Flake & Nugget: Superior Reliability
High Quality Manufacturing
All Scotsman machines are manufactured and tested at our award-winning facility in South Carolina to ensure you get a reliable machine that works exactly like it should
Assembled in the USA
Award winning Fairfax, South Carolina Facility
ISO9001:2015 accredited
All machines run tested before shipment

## Slide 23: Flake & Nugget: Superior Reliability
Standing Behind Our Quality
Scotsman provides a 3-year parts and labor warranty on all components for 15” and 20” units
3-year parts and labor warranty on all components
Warranty valid in North, South & Central America for commercial installations
Residential applications :
  1 year parts and labor

## Slide 24: Flake & Nugget: Environmentally Friendly
Lower Operating Costs
Uses R-134a refrigerant
  Does not deplete ozone layer
Lower energy and water consumption compared to cube machines
Recyclable aluminum alloy side panels
  Same durability and corrosion resistance as stainless-steel
Meets US Safe Drinking Act low lead requirements

## Slide 25: Undercounter Nugget: About The Ice
Increased Profitability
  Consumer preferred
  Lower cost by 1/3 per 100 lb. of ice
    Uses 40% less water (vs. cube)
    Uses 15% less energy (vs. cube)
  Lower beverage costs
    9% - 20% higher displacement
      Use less syrup/beverage
Scotsman’s Nugget Ice:
Soft
Easy to chew
Rapid cooling
Slow-melting
Absorbs the flavor of beverages

## Slide 26: Undercounter Flake: About The Ice
Presentation & Preservation
Flake Ice is a Smart Choice for:
Blended cocktails
Salad bars
Produce, seafood, and meat displays
Therapeutic use in healthcare facilities

## Slide 27: Undercounter Flake & Nugget: Applications
Ideal for Placement in:
Restaurants
Café
Bar
Offices
Break Rooms
Cooler Filling
  Construction, HVAC workers
Schools
Health Club/Spa
Laboratories