## Slide 1: Technical Service Training
15” and 20” Undercounter Flaker and Nugget Machines
Notes: Welcome to a presentation on Scotsman’s self-contained ice machines, the UF and the UN 15 and 20 inch wide flake and nugget ice machines.

## Slide 2: Service Support
Technical Service 1-800-533-6006
Check out our mobile ready website
www.scotsman-ice.com/service
Notes: Service support is a few clicks away on the internet. Scotsman-ice.com/service.
Scotsman’s recent products are also marked with a symbol that, when read by your smart phone, will take you directly to the service information menu at Scotsman’s website.
At the website there are service manuals, illustrated service parts, and service bulletins.

## Slide 3: Technical Service Virtual Business Card
Notes: Here is an image of a QR code that will connect you directly to the warranty verification section of Scotsman’s website.
While all products are supplied with a user manual, sometimes it isn’t available at the site and, for example, you need to clean the machine. The user manual is on the website and easily found there. So, cleaning instructions as close as your phone.

## Slide 4: Training Agenda
Introduction
Installation
Operation
Maintenance
Diagnostics
Taking the unit apart
Notes: In this meeting you will learn about the UF and UN models. You will learn how to install them. How they work, how to maintain them and a lot of detail on how to take them apart. There will be a diagnostic section to help you find out what the cause of a potential malfunction is. And at the end a look inside.

## Slide 5: Introduction
Undercounter type, Flake or Nugget ice forms
Three capacities each
  First two numbers
  Second two numbers are cabinet widths, 15 or 20 inches
Flaked Ice | Nugget Ice
UF0915 | UN0815
UF1415 | UN1215
UF2020 | UN1520
Notes: As in other models, the UF prefix is for an Undercounter Flaker, while the UN prefix means Undercounter Nugget.
Flaker means it makes flaked ice. Flaked ice is a soft ice that is easily packed around irregular objects, like test tubes and food.
Nugget means it makes the round, pellet like Scotsman nugget ice form. It is used in soft drinks and is easily chewed.
There are three models each, the numbers 15 and 20 are the cabinet widths.
All are just under 32 inches high, without legs. With legs, they are just under 38 inches tall.

## Slide 6: Introduction
Air cooled only
R-134a
Front air in and out
Stainless steel evaporator
Solid grease top bearing
Auger load monitoring
Cleaning indicator
Cleaning mode
Water sensor
Photo eye ice level control
QR code behind front panel. Connects to warranty registration and unit specific service resources.
Notes: These smaller models are air cooled only. They use R-134a for a refrigerant, the air flow is front in and out so they may be built into a cabinet.
The evaporator is rugged stainless steel, and the top bearing uses a solid grease, which is designed to keep the grease in the bearing.
Auger load monitoring is standard. That feature will shut the auger motor down if the current draw is either too high or too low.
There is a cleaning indicator, which is not visible the front. A cleaning mode is built in to the control system, to make it easier to clean.
A water sensor is critical for this type of machine, these models use a conductivity probe for that.
And the bin control is a photo eye system.

## Slide 7: Components
Controller’s lights and switches
Notes: Removal of the front panel exposes the controller light and switches, which are mounted to the right of the electrical box.

## Slide 8: Components
Condenser
Notes: The intake side of the air cooled condenser is on the right, air flows into it from the louvered front pane, and if not resting on the floor, from below.

## Slide 9: Components
Fan motor and blade
Notes: The fan motor and blade are on the discharge side of the condenser, just behind t he electrical box.
Air will be forced out the front. A lower amount will be discharged out the back panel.

## Slide 10: Components
Electrical Box
  Metal cover
  Open at the back
Caution: Disconnect electrical power if working in this area.
Notes: The electrical box has a metal cover, which is open at the back. All terminals are insulated, but care should still be taken when working on a live unit.

## Slide 11: Components
Controller, Fuse Holder and Transformer
Caution: Disconnect electrical power if working in this area.
Notes: Removing that box cover allows access the transformer, fuse holder and controller.

## Slide 12: Components
Chute Cover
Notes: Removing the top panel and door or just opening the door gives access to the chute cover.
The chute cover is held on to the back of the storage in by two thumb screws.

## Slide 13: Components
Chute and Photo Eyes
Caution: The moving ice sweep could pose a rotation hazard.
Disconnect electrical power when working in this area.
Notes: When the chute cover, door and top panel are removed, the chute and photo eyes are exposed.
The chute cover must be removed to get to the photo eyes. It is not necessary to remove the top panel or door to get to the photo eyes.

## Slide 14: Components
Ice Sweep
Breaker
Float Valve and Reservoir
Notes: With the top panel off, the ice sweep, ice breaker, float valve and reservoir are visible. The ice sweep and ice chute can be removed without taking off any more parts. The reservoir must have the back panel removed for its removal.

## Slide 15: Components
Water, Drain and Power Cord
Notes: All models are equipped with a power cord and a water inlet tube.
A condensate and meltage drain fitting is also on the back panel.
The power cord is 5 feet long, as is the one quarter inch water inlet tube.
The drain fitting is three quarters female pipe thread.

## Slide 16: Components
Reservoir
Water Sensor
Compressor
Notes: Taking the back panel off exposes the water reservoir, the water sensor in the reservoir and the compressor at the bottom.

## Slide 17: Components
Connect Potable Water
  Water Conductivity Rating
    A minimum of 10 micro Siemens/CM
  Ultra pure water will not work
    Such as DI
  ¼ inch tubing
  Flush before connecting
Connect Drain
  Slope to building drain
  Maintain air gap per codes
  Vent when needed
Connect Power Supply
  NEMA 15P plug
Notes: Installation is simple. The unit needs power, water and drain.
Connect a drain per local code. A three quarter female pipe thread fitting is provided. It is plastic, so do any soldering of drain components separately from it.
The water supply must be potable, and have a Water Conductivity:
Minimum of 10 micro Siemens per CM
The water inlet tubing is one quarter inch. Attach to a water supply using compression fittings of the correct size.
Plug the power cord into the standard 115 volt outlet, it is recommended that it is on its own circuit.

## Slide 18: Start Up
Remove front panel
Switch on water supply
  Confirm water level is correct, and not overflowing or underfilling reservoir
Switch on power supply
If not operating, push On to start
Add water to bin, check for drain leaks
It may take several minutes for ice to begin falling into the bin
Notes: Start up is also simple.
Switch on the water supply, and observe that the reservoir fills up and the float valve shuts off.
Connect electrical power.
If not operating, push and release the On button to start the unit.
Flush the bin with water and check for draining and leaks.
It may take several minutes for ice to form, but warm air will flow out the left front.

## Slide 19: Start Up
Check ice level sensor function
  Temporarily block light between sensors
  Status light should blink green
A full bin may take a full day
Notes: It is a good idea at start up to confirm that the ice level sensor system is working. Place something between the photo eyes and the status light should blink green. Clear that area and allow the unit to make ice. It could take a full day to fill the ice storage bin to the level in the photo.

## Slide 20: Electrical
Controller operates
  Compressor
  Fan motor
  Auger motor
Two sensors
  Water
  Bin level
Auger motor independent of compressor and fan
  On during shut down to clear evaporator of ice
Notes: This is a simple ice machine. It has three motors, the compressor, the fan motor and the auger motor. There are two sensors, a bin level sensor and a water sensor.
There are no pressure controls.
The controller will operate all motors if the bin sensor is calling for ice and the water sensor indicates there is water in the reservoir.
At shut down, the compressor and fan motor stop but the auger motor continues to operate for a minute to clear the evaporator of any ice. That makes a restart easier on the auger motor.

## Slide 21: Refrigeration
Notes: The refrigeration is also simple, it is a cap tube system.
The hermetic compressor forces high pressure hot discharge gas into the air cooled condenser, where significant heat is released and the gas changes to a liquid.
The liquid refrigerant is forced thru the capillary tube to where it enters the evaporator, there it expands and absorbs heat from the cylinder walls and the water inside.
Ice crystals form and are pushed up by the auger and thru the breaker as ice.
The now low pressure refrigerant flows back to the compressor and the cycle continues as long as the control system calls for ice.
System pressures do not change, this is a steady state system.

## Slide 22: Refrigeration
No access valves
  Pressures sometimes needed
  Normal pressures for new, clean machine with full charge and making ice normally
Model Discharge PSIG Suction PSIG Discharge PSIG Suction PSIG 70/50 70/50 90/70 90/70
UN0815 or UF0915 106-110 10-11 143-148 13
UN1215 or UF1415 189-191 8-9 225-230 11
UN1520 or UF2020 108-114 1-4 151-159 4-6
Notes: Although these models do not have access valves, sometimes it may be necessary to add them for a full diagnosis.
These are the system pressures, for a new, clean and fully functional unit. They are by model with two temperatures.
70/50 means seventy degrees F. air temperature and fifty degrees F. water temperature. These temperatures were in a test room under ideal conditions, so the field numbers may vary slightly. Do not feel the machine is undercharged if the numbers you get are slightly different.

## Slide 23: Ice Making System
Water Level
Breaker
Auger Motor
Evaporator and Auger
Reservoir and Float Valve
Gear Reducer
Notes: The gear reducer, evaporator and auger form the freezing section of these machines. The gear reducer rotates the auger slowly, about 10 rpm, and as ice is formed and discharged, replacement water enters at the bottom.
The auger is thrust down by the force of ice making. That thrust is taken up by the bearings in the gear reducer. The top bearing is there to provide alignment.
The water level in the evaporator is the same water level as is in the water reservoir.

## Slide 24: Continuous Flow Ice Making
Flaked or Nugget ice
  Evaporator tube contains auger and water
  Heat removed from the water until ice crystals form
  Slowly rotating auger forces compressed ice up and thru the breaker
  Extruded thru the breaker’s restrictive holes or slots
  Water flows in at the bottom of the evaporator tube to keep the heat load in balance
  Continuous flow of water in and ice out
Notes: The key to the proper operation of this continuous flow ice machine is the balance between the ice out and the water in.
The refrigeration system will be taking the same amount of heat out, water present or not. So it is critical that water, or heat load, continue to be provided.
Nugget ice has more water squeezed out when comparted to flaked ice. And both are much wetter and softer than cubed ice, which is formed in a completely different process.
If the water supply would fail, and the unit continue to run, the auger motor will be overloaded, as the ice will be much harder.
If the auger would slow down or stop, and the unit continue to run the auger motor will be overloaded.

## Slide 25: Water and Mineral Scale
Water supplies can have suspended solids and dissolved solids.
  Suspended solids can be filtered out
  Dissolved solids are part of the water, but ice machines separate them by the ice making process
    Cube ice machines do that by freezing the pure water first, leaving the mineralized water behind.
    Flaked and nugget machines are different, as the water going in is discharged as ice. But they get coated by minerals from ice making too.
Ice machines need to be treated with scale remover
  Food grade acid dissolves the scale
Notes: We are often asked, how long does an ice machine last? The answer is not a simple number of years. Their lifespan depends on three basic items: water quality, run time and maintenance.
If they are on a water supply with high mineral content, are running 24/7, and get no maintenance their life will be shorter than those on average water, running an average amount of hours and are cleaned regularly.
Filters are great for suspended solids, but they cannot filter out the dissolved solids that are part of the water. Ice making causes many of those dissolved solids to fall out of the water and then they can stick to the machine and need to be cleaned out with scale remover.

## Slide 26: Water and Mineral Scale
Notes: The two photos are of actual flaker parts from a couple of field units. The left on is an auger, stained with scale. It is supposed to be bright and shiny.
The right image is the inside of a flaker evaporator, heavily stained with mineral scale. Like the auger, the inside of the evaporator is supposed to be bright and shiny stainless steel. A great deal of machining was used to make it that way and now it is rough and scarred.

## Slide 27: Water and Mineral Scale
Scale on the evaporator wall and auger increases the load on the gear reducer
  Normally, ice slides straight up the wall and is extruded.
  When the wall is covered with scale, ice may not slide up the evaporator, instead it revolves with the auger and stays too long under refrigeration, becoming a solid that is hard to extrude.
  That increases auger motor amp draw.
  A possible symptom is a loud noise during ice making
    Known as a rotating freeze.
Notes: Why be concerned with scale build up? It is because the ice in the flaker freezer is supposed to slide easily up the evaporator wall and be extruded thru the breaker. When there is scale on the parts, the ice has a harder time getting out of the evaporator, causing extra load on the gear reducer, usually increasing its current draw.
If the ice, instead of moving up the wall, starts to spin with the auger, it stays in the evaporator too long, freezing into a more solid form and so becomes much harder to extrude. The result is a very heavy load on the gear reducer and usually a very loud noise from the machine. The noise is a symptom of what is called a rotating freeze.

## Slide 28: Auger Load
Auger motor current is monitored by the controller
  Will shut the unit down if too high or too low
High amps can be caused by
  Very significant scale on auger and evaporator
  Component wear, possibly gear reducer or bearing
Low amps can be caused by
  Open motor winding
  Open motor overload
  No power to motor
Notes: The controller for these machines has load monitoring for the auger motor. It continually checks for operating current draw and will shut the unit down if it is too high or too low.
High current can be from the scale mentioned earlier. Or it can be from component wear..
Low amps are almost always because of an open winding in the auger drive motor, or there is no power to the motor because of a relay failure in the controller. Another cause can be an open motor overload from overheating. Normal motor temperature is about one hundred and seventy five degrees F.

## Slide 29: Cleaning and Maintenance
Three areas:
  Air cooled condenser
  Evaporator and water system
  Photo eyes
Air intake is on the right
Brush lint and dirt from fin surface
  Use care, do not damage fins
  Vacuum and / or blow out
Imbedded grease must be removed with coil cleaner
Sanitize Indicator light switches on after 6 months of power up time
Notes: We have talked a lot about scale and the need for cleaning. What about how to clean the machine to get rid of scale and to take care of any other maintenance?
There are three areas to clean. The air cooled condenser, the evaporator and the photo eyes.
The condenser’s air intake is on the right and there is no filter, so the fins will gather lint and grease on that side. It needs to be brushed off to get rid of the lint and if there is grease a condenser cleaner will be needed. Blowing it out must be done carefully so the fins are not damaged.

## Slide 30: Cleaning and Maintenance
Evaporator and Water System
  Minerals in the water supply flow thru the system
  Over time, they begin to coat the ice making and water surfaces
  This mineral scale must be removed using scale remover
Notes: The mineral scale must be removed by making and using scale remover solution. Liquid scale removers are more effective than powders, but both must be mixed with the correct amount of water. Making the solution stronger does not make it better! In fact, trying to clean a flaker with too strong a solution will cause it to bog down and might stall out, all while making a hell of a noise.
Scotsman has Clear 1, a nickel safe cleaner good for all ice machines.

## Slide 31: Scale Removal Step by Step
Shut unit off
Discard ice
Remove top, front and back panels
Shut water supply off
  At source or use the reservoir lever to raise the float
Drain evaporator and reservoir
  Disconnect outlet hose, water will drain into condensate pan and then out of the unit.
  Note: If the unit was pulled out, there must be a drain tube connected to the building drain.
Reconnect outlet hose
Notes: Cleaning begins with shutting the unit off and discarding any ice.
Remove the top, front and back panels. If built in the unit must be pulled out. And if pulled out there still must be a drain as water and cleaning solution will be flowing out.
Shut the water supply off, either at the source of using the lever on the reservoir that lifts the float.
The evaporator and water reservoir must be drained so the cleaning solution can contact the parts
The outlet hose must be reconnected.

## Slide 32: Resevoir Outlet Hose
Hose must be connected to plug molded into base or water / cleaning solution will leak out
  Located to right of evaporator
Notes: The outlet hose connects one leg to a closed plug on the base of the evaporator pan. If not connected all the expensive cleaning solution will leak out down the drain.

## Slide 33: Scale Removal Step by Step
Mix 2.5 ounces of Scotsman Clear 1 scale remover and one quart of water.
  Only mix correct ratio.
  MORE is NOT better!!!!
Pour that solution into the water reservoir.
Push both On and Off buttons in until the unit starts
  The clean light will blink
  The auger motor will start
Notes: For this model, mix two and a half ounces of Clear 1 scale remover to a quart off potable water. Do not mix it stronger!
Pour that into the reservoir until it is full.
Push and hold both on and off buttons together until the unit starts. The clean light will blink and the auger motor will start.

## Slide 34: Scale Removal Step by Step
When the compressor starts, add cleaning solution to the reservoir as ice is made. When all of the solution is used, turn the water supply back on.
The unit will stay on during the cleaning mode and then shut off.
Shut water off again and drain evaporator and reservoir again.
Wash out the bin and rinse with water to flush out the drain.
Reconnect reservoir outlet and either switch water supply on and restart ice making or sanitize the unit.
Notes: The unit is now in a cleaning mode. The auger rotates in the solution to better stir it during this half of the cleaning mode.
As the slide says, the compressor will start and then ice making will occur. As it does, keep pouring in cleaning solution until it is gone. Then open up the water supply.
The cleaning mode is complete when the compressor stops.
Shut the water off and drain the evaporator again. Then reconnect the outlet hose and either restart ice making or sanitize the unit.

## Slide 35: Sanitization
The ice making system and the ice storage area must be sanitized on a regular schedule.
Use potable water and approved sanitizer.
Follow the same procedure as used for scale removal.
  Substitute approved sanitizer solution for scale remover.
Wash out the ice storage bin area and the ice chute area with sanitizer before restarting ice making.
Using the cleaning mode resets the De-Scale indicator light.
Notes: Sanitize after scale removal. Use an approved sanitizer and run it thru the machine like the scale remover.
Wash all ice making surfaces with sanitizer and also the inside of the ice storage bin. Flush out the bin with hot water to be sure the drain is working properly. If pulled out, do this after it is reinstalled in its normal position to be sure the drain is working correctly.
Finally, using the cleaning mode resets the cleaning indicator light.

## Slide 36: Photo Eyes
Access them by removing the chute cover at the back of the bin.
Pull the white clip up to release the rubber holder.
Carefully wipe clean the clear lens inside the rubber holder.
  Use a soft cloth, not a screwdriver!
Notes: The photo eyes can become covered with mineral scale or even dirt. They must be checked and cleaned if dirty.
To check, remove the chute cover from the back of the bin.
Pull the white clips up and release the eye holders.
Check and clean as needed. Do not scratch the lenses.

## Slide 37: Diagnostics and Service
Notes: In the diagnostics section, you will hear a lot about water causing certain failure modes. This is because in the recipe for ice, water is the biggest component. To make ice, we use water, mechanical refrigeration and an electrical system to operate and control ice making.

## Slide 38: Indicator Lights
Code or Light Action | Condition | Suggested Action
Power light is ON | Normal | None
Status light is ON | Making ice | Normal when bin is not full
Water light is OFF | Normal | None
Water light is blinking ON and OFF | No water sensed | Check water supply to unit, possibly restricted by clogged filter
Status light blinking red | Auger motor current draw out of spec | Reset controller and check auger motor amps. If out of spec but operational, clean water system and recheck. Replace motor or complete gear motor if auger motor amps are still out of spec.
De-Scale light is ON | Unit has not been cleaned for at least 6 months | Clean unit per manufacturer’s instructions
Notes: This product has some indicator lights to assist in the diagnostic process. They are not visible unless the front panel is removed.
There are four lights: Power, Status, Water and Clean.
When the power light is on, that is normal.
When the status light is on, the unit is in ice making mode. No action is needed unless it is blinking and the bin is not full.
When the water light is off, that is normal. No action is needed unless the water light is on.
The status light is normally steady. If blinking, the auger motor current is out of spec. The controller should be reset by turning electrical power off and then on. Then check auger motor current. There will be more details on the next page.
The clean light is normally off, but switches on after 6 months of power up time since the last cleaning.

## Slide 39: Status Light: Codes
Light Code | Meaning
Off | Not in ice making mode
On Steady | Making ice
Blinking green | Shutting down or bin full
Blinking red, one long, one short, every 5 seconds | Auger motor overcurrent, first notice
Blinking red, one long, two short, every 5 seconds | Auger motor overcurrent, second notice
Blinking red, one long, three short, every 5 seconds | Auger motor overcurrent, third notice
Blinking red, two long, one short, every 5 seconds | Auger motor under current, first notice
Blinking red, two long, two short, every 5 seconds | Auger motor under current, second notice
Blinking red, two long, three short, every 5 seconds | Auger motor under current, third notice
Notes: The status light has its own codes.
Off means it is not in ice making mode.
On steady is making ice.
Blinking green is when the unit is shutting down or the bin is full.
Blinking red is when the auger motor current is out of spec. It normally draws about point four tenths amp. If much higher than that, the status light will be blinking red with a one long blink, followed by on, two or three short blinks.
If the auger motor current is zero or near that, then the status light will be blinking red with two long blinks, followed buy one, two or three short blinks.

## Slide 40: Diagnostics
No ice, unit condition:
  Power light is off
  Check for power to unit
  Check for open fuse
    2 amp, 250 volt
  Check for open transformer
Notes: Let’s go thru some no ice service call scenarios.
In this one, the power light is off and so are all the others.
To diagnose, check for power to the unit, or an open fuse or transformer. If there is 12 volts power from the transformer, and the fuse is good, then the controller could be at fault.
However, testing of returned controllers showed that nearly all of them work properly when reinstalled in a unit.

## Slide 41: Diagnostics
No ice, unit condition:
  Power light on
  Water light off
  Status light blinking green
  Compressor and Auger motor are OFF
Cause: Controller has sensed bin full, but the bin is not full
  Infrared sensors may have scale on the lens
  Infrared sensors may have failed. Clean first, if no improvement, replace sensor set
Notes: Proper diagnostics are the key to a short and successful service call. Finding the root cause of the malfunction and correcting just it are critical. This section will help with that.
A no ice call is likely to be the most common type on an ice machine. In this case, it is found that the compressor and the auger motor are OFF. The first step after that is to identify any trouble codes. A code chart is on the product, just above the controller.
In this case the status light blinking green indicates a full bin. But the bin is not full.
The on and off mode of the unit is controlled by the ice level sensors. If they indicate a false bin full, then the unit will shut off and there will be no ice.
The sensors are light sensitive and their lenses must be clean.

## Slide 42: Diagnostics
No ice, unit condition:
  Power light on
  Water light blinking red
  Auger motor and compressor are OFF
Cause: Controller has sensed no water in the reservoir
  Check for water supply turned off
  Check for water supply restricted by plugged filter
  Check for water in reservoir
Notes: As noted earlier, water is critical to the proper operation of this ice system. To prevent damage, a water sensor safety has been incorporated into the design. It is a conductivity sensor, which, when dry signals to the controller that there is no water.
So, if the water light is on, check for the water supply turned off, or restricted by the water filter which probably has not been changed since the unit was installed, or maybe even the prior unit.

## Slide 43: Diagnostics
No ice, unit condition:
  Unit off
  Status light is blinking red
Cause: Auger motor either over or under amp draw spec
Normal amps are about .4 (four tenths)
  One blink, and then one, two or three is an over amp failure
  Two blinks, and then one, two or three is a very low or no amp failure
Three blink code means the unit is locked out and must be manually reset
  Cycle power off and on to reset
Notes: An unusual condition is when the auger motor current draw is out of spec. If it draws too much or too little, the controller will stop and try three restarts. If they all fail, it does not restart again and must be reset manually.

## Slide 44: Diagnostics
No ice, unit condition:
  Power and status lights are green and not blinking
  Auger motor is operating
  Compressor is off
Check for
  Power to compressor, if none, controller relay may not be working
  Overheated compressor, due to dirty condenser or fan not working, or low refrigerant charge
  Open windings on compressor
  Start relay failure
  Start capacitor failure
Notes: The controller’s indicators show that the unit should be making ice. The auger motor is on and rotating the auger but there is no refrigeration effect.
That is because the compressor is off.
Compressor diagnostics begin with power to it. If none, the controller relay is suspect. If there is power, then the compressor may have temporarily overheated. That can be from low refrigerant charge or the fan stopped turning.
The start relay could have failed, causing the compressor to not start and overheat.
A permanent failure is open windings in the compressor.

## Slide 45: Taking the Unit Apart
Panels to remove
  Front
  Top
  Back
Removing side panels does not improve access.
Notes: This section will give you familiarity with how to take the product apart.

## Slide 46: Taking the Unit Apart
Condenser Fan
  Unplug from electrical power
  Separate fan motor lead from harness
  Four screws hold fan brackets to shroud
Notes: Unplug the unit or disconnect electrical power.
Remove the front panel.
The condenser fan is held onto the condenser shroud with four screws. A one quarter inch nut driver would be a good tool to use to take them out.
Then disconnect the harness behind the fan motor and pull the motor, blade and brackets out.

## Slide 47: Taking it Apart
Fuse
  Unplug from electrical power
  Remove electrical box cover
  Twist fuse holder to release and replace fuse
    2 Amp, 250 Volt
Notes: An inline fuse is used to protect the controller.
First, disconnect electrical power.
Remove the front panel.
Then remove the electrical box cover. The fuse holder is right there.

## Slide 48: Taking the Unit Apart
Controller
  Unplug from electrical power
  Remove electrical box cover
  From the condenser side, squeeze the stand off catches together and push the controller back
  Disconnect from electrical harness and remove controller
Notes: If you have confirmed that the controller is broken and must be replaced, then remove the front panel.
Unplug from electrical power.
Remove the electrical box cover.
And then, from the condenser side, squeeze the white plastic standoffs together and push them back to release the controller from the sheet metal.
Disconnect from electrical harness and remove from the unit

## Slide 49: Taking the Unit Apart
Photo Eyes
  Unscrew two thumbscrews and remove Chute Cover
Notes: To replace photo eye set, begin by taking off the front and top panels. If the unit is built it, it must be pulled out.
Remove the chute cover.

## Slide 50: Taking the Unit Apart
Photo Eyes
  Unplug from electrical power
  Pull up on white retaining clips
Notes: Disconnect from electrical power and pull up on the left and right white clips to release the black rubber photo eye holders.

## Slide 51: Taking the Unit Apart
Photo Eyes
  Pull lens and cable from black rubber lens holder
  Disconnect from electrical harness
Notes: Pull the lens out of the rubber holder and disconnect from the harness.

## Slide 52: Water Reservoir and Float Valve
Water Sensor
  Remove screw holding sensor to reservoir
  Lift sensor and probes out of reservoir
Notes: The water sensor is at the end of the reservoir. Remove the top panel, and again, if the unit is built in it must be pulled out for this.
Remove one screw and lift the sensor from the reservoir.
Disconnect wires from sensor.

## Slide 53: Taking the Unit Apart
Ice Sweep
  Unplug from electrical power
  Rotate CCW to remove
Notes: Unplug or disconnect electrical power.
Remove the top panel.
Rotate the ice sweep counterclockwise to remove.

## Slide 54: Taking the Unit Apart
Breaker
  Unplug from electrical power
  Remove four hex head screws
  Lift off evaporator
Notes: The ice breaker can now be removed.
Unscrew four socket head screws and lift the breaker up and off the unit. Socket size is one quarter inch.

## Slide 55: Taking the Unit Apart
Auger
  Be sure electrical power is off
  Shut water off and drain reservoir and evaporator
  Pull auger out of evaporator
Notes: It is very important to shut the water off and drain the evaporator before pulling the auger up and out of the unit.

## Slide 56: Evaporator
Notes: This view of the machine shows what it looks like when the auger has been removed. Note the vertical lines inside the stainless steel evaporator. And also the stationary part of the water seal at the bottom.
The vertical lines are there to help guide the ice up the evaporator wall and to keep it from rotating with the auger.

## Slide 57: Taking the Unit Apart
Evaporator or Gear Reducer
  Unplug from electrical power
  Remove back panel
  Shut water off and drain reservoir
  Attach access valves and recover the refrigerant charge
  Disconnect auger motor from electrical harness
  Remove screws holding gear reducer base to pan
Notes: Removal of the evaporator requires several steps.
First, unplug or disconnect from power. Then remove the top and back panels and shut the water supply off. Then drain the water from the evaporator.
The bottom of the evaporator is not accessible while in the machine, so the assembly must be removed.
The evaporator’s inlet and outlet must be disconnected, attach access valves and recover the refrigerant charge.
Unplug the auger motor from its harness.
Remove the screws holding the gear reducers base to the unit.

## Slide 58: Taking the Unit Apart
Pull back suction line and evaporator inlet line insulation
Cut or unbraze at locations marked
Lift assembly out of unit
Notes: Uncover the suction and evaporator inlet tubing as shown.
Cut or unbraze at the locations marked.
Lift the assembly out of the unit.

## Slide 59: Taking the Unit Apart
Remove four socket head screws on the side of the evaporator bottom
Notes: With the gear reducer and evaporator assembly out of the unit, the evaporator can be separated from the gear reducer.
Remove the four socket head screws holding them together.
Lift the evaporator off of the gear reducer.

## Slide 60: Taking the Unit Apart
Lift evaporator off gear reducer’s adapter
Stationary half of water seal remains in evaporator
Notes: At this point, the water seal may be replaced. The stationary half remains in the bottom of the evaporator as shown.

## Slide 61: Water Seal
Two-part seal
  Stationary part in evaporator
  Rotating part on auger
Pull stationary half out of evaporator
Remove rotating half from auger
Notes: The water seal is one used by Scotsman for many years. It is a two-piece face seal, with a rotating half that spins with the auger and a stationary half that is fixed in the evaporator tube. Pull the stationary half down and out of the tube. Then remove the old rotating half from the auger.

## Slide 62: Water Seal
Assembly
  Wet stationary half
  Insert 1 ¼ to 1 3/8 into bottom of evaporator tube
    Adapter will push seal to correct height
      About an inch and a half
Notes: Wet the new stationary half with water or very light food grade lube. Insert it about an inch and a quarter to an inch and three eighths into the bottom of the tube, brass side down. When the evaporator is placed onto the adapter, that will locate the seal to the correct position. It is important to not insert it too far.

## Slide 63: Water Seal
Assembly
  Clean auger shoulder
  Add small bead of food grade RTV sealant to shoulder
  Push rotating half of seal onto auger
    Do NOT touch sealing surface
    Push on outside of ring
    OK to wet inside of rubber ring to aid in sliding onto auger
Rotating Seal
Notes: On the auger, remove the old seal, clean up the shoulder of the auger where that seal was mounted and add a small bead of food grade sealant to the auger’s shoulder. Then, wet the rubber ring of the seal and carefully push it onto the auger. Do NOT touch the sealing surface. Push it on as far as possible. The sealant will compress and fill the very small space left when the seal is on all the way.

## Slide 64: Sealant on Auger
Sealant on Auger to Fills in Between Water Seal and Auger Shoulder
Notes: The sealant is not for water leaks but to protect the auger from pitting.

## Slide 65: Summary
This ice system has
  Two ice forms, flake and nugget
  Three ice capacities in each form
  Two cabinet sizes
Ice making is by continuous flow
Ice on and off by photo eye
Water sensor in reservoir
Air cooled only
R-134a, No service ports
Auger motor current monitor
Notes: In summary, these are very small flaked and nugget ice machines. There are two ice forms and three ice capacities each.
Like all other Scotsman flakers, they are continuous flow ice machines. They do not have a harvest cycle.
They are controlled by photo eye sensors, have a water sensor and auger motor load monitoring safeties.
Air cooled only and use R-134a as the refrigerant.

## Slide 66: Questions?